ENGR 224 – Thermodynamics

Final Exam – Outline	Spring 2011

Chapter 9 – Power Systems

- Vapor Power Cycle: The Rankine Cycle

  - Closed cycle: working fluid is recycled

  - Water is usually the working fluid

  - Evaporator and condenser used for isobaric heat transfer steps

  - Minimizes cavitation in the pump and provides for the possibility of superheating the turbine feed to increase turbine effluent quality.

  - Ideal Rankine Cycle

    - Pump and turbine are isentropic

    - Condenser effluent is a saturated liquid

    - Turbine feed is a saturated vapor

  - Improvements

    - Superheat: improves turbine effluent quality and increases (th

    - Supercritical: increases (th, high T & P requires expensive materials

    - Reheat: decreases (th unless used with regeneration, but increases turbine effluent quality

    - Regeneration: Preheat boiler feed using HP turbine effluent

      - Increases (th

      - Great in combination with reheat

      - Open and closed feedwater heaters are used

    - Binary: Two Rankine Cycles with different working fluids

      - Big increase in (th

      - Can reach high temperatures and efficiencies without using high pressures

    - Cogeneration

      - Use some or al of the HP turbine effluent in another process.

      - Saturated liquid is returned from the other process.

- Gas Power Cycles: The Brayton Cycle

  - Air-Standard Assumptions

    - Air is the working fluid and it behaves as an ideal gas

    - Modeled as a closed cycle

      - A 2nd HEX is used to restore the working fluid to its initial state and close the system

    - Internal combustion replaced by external combustion and a HEX

    - Both HEX’s are isobaric

    - Ideal Cycle: compressor and turbine are internally reversible

  - Cold Air-Standard Assumption

    - Heat capacities are constant and hallways have the value at 25oC.

    - GREATLY simplifies analysis, but preserves trends

    - Compression ratio is the key parameter

  - Improvements

    - Regeneration

      - Hot turbine effluent is used to preheat the feed to the combustor

      - Improves efficiency at low compression ratios

      - Regenerator Effectiveness: ( = fraction of maximum possible heat transfer that is actually achieved in the regenerator

    - Reheat

      - Reheat HP turbine effluent

      - Avoids extremely high temperatures, but decreases (th unless used in combination with regeneration

    - Multi-Stage Compression with Intercooling

      - Reduces work requirement for the compression, but decreases (th unless used in combination with regeneration.

Chapter 10 – Refrigeration and Heat Pump Systems

- Vapor Compression Refrigeration  (VCR)

  - Ideal VCR Cycle

    - Isobaric condenser and evaporator

    - Isentropic compressor

    - Isenthalpic expansion valve

    - Condenser effluent is a saturated liquid

    - Evaporator effluent is a saturated vapor

  - Refrigerant Selection Criteria

    - Cost, chemical stability, corrosiveness, toxicity, flammability

    - Large (Hvap is desirable to minimize mass flow rate

    - Vapro pressure or saturation pressure is the most important criterion

  - Cascade  VCR

    - Two separate refrigeration cycles usually using different refrigerants.

    - Advantages: High COPR and can reach low temperatures

    - Disadvantages: expensive

  - Multi-Stage VCR

    - Two cycles using the same refrigerant

    - Flash drum is used to separate and recycle saturated vapor

    - Instead of HEX, streams are mixed

    - Advantages: Higher COPR than cascade

    - Disadvantages: expensive, cannot reach temperatures as low as cascade can

- Vapor Compression Heat Pumps

  - Same reservoir temperatures and therefore same working fluid as VCR

  - Only difference is the objective: QH

  - Reversing valve makes it easy for a home heat pump to also function as a home air-conditioner

- Gas Refrigeration Cycles

  - Less efficient than VCR, but much lighter weight

  - Can easily reach cryogenic temperatures (T < 150 K)

  - Reverse the Air-Standard Brayton Cycle

  - Regeneration

    - The key to reaching cryogenic temperatures

    - Pre-cool the turbine feed using working fluid after it has absorbed QC from the cold reservoir

    - This reduces the temperature of the turbine effluent, which is the lowest temperature that the cycle reaches.

      - Regenerator Effectiveness: ( = fraction of maximum possible heat transfer that is actually achieved in the regenerator